## Slide 1: Automation with Napalm

## Slide 2: Oversikt
Why automate?
High level overview
Hva er Napalm?
Vendor support – hvilken leverandører er støttet?
Hva kan vi gjøre med Napalm ?
Demo

## Slide 3: Hva er Napalm?

## Slide 5: Hva kan man gjøre med Napalm - Getters
https://napalm.readthedocs.io/en/latest/support/index.html#getters-support-matrix

## Slide 6: Hva kan man gjøre med Napalm?
https://napalm.readthedocs.io/en/latest/support/index.html#general-support-matrix

## Slide 7: IOS Requirements
Netmiko må finnes på serveren man kjører script
SCP og archive på managed device
rtr1#sh run | s archive
archive
path flash0:bkup-$h-$t
write-memory
rtr1#sh run | i scp
ip scp server enable
For more details
  https://napalm.readthedocs.io/en/latest/support/ios.html

## Slide 8: NXOS Prereq
conf t
  feature scp-server
  feature nxapi
  no nxapi http
  nxapi https port 65000
  end
rtr2# show feature | egrep "nxapi|scp"
nxapi 1 enabled
scpServer 1 enabled
rtr2# show nxapi
nxapi enabled
HTTPS Listen on port 65000
Certificate Information:
Issuer: /C=US/ST=CA/L=San Jose/O=Cisco Systems Inc./OU=dcnxos/CN=nxos
Expires: Feb 23 08:43:27 2021 GMT

## Slide 9: Optional arguments – viktig å vite
Bruk disse hvis man må bruke non-default settings, eksempel:
  Default for IOS er SSH, telnet med optional transport
  Nexus, default transport er HTTPS, hvis man skal bruke http, eller et annet port for HTTPS, eksempel vi skal gå gjennom bruker port 65000.
Mer detaljer:
  https://napalm.readthedocs.io/en/latest/support/index.html#optional-arguments

## Slide 10: Napalm Demo Topology

## Slide 11: Getters Demo
Eksempel viser:
get_facts()
get_lldp_neighbors()
get_bgp_neighbors()
get_bgp_neighbors_detail()
get_bgp_neighbors_details er kun implementer i IOS https://napalm.readthedocs.io/en/latest/support/index.html#getters-support-matrix så vi får runtimeexception i NXOS.

## Slide 12: Config Merge Demo
Add a loopback to both rtr1 and rtr2
Advertise loopback over BGP

## Slide 13: Tips
Remember Close, også når det skjer feil, feil passord, device down, osv.
Tenk: reuse, reuse.
Tenk: Code readability
Gotcha, hvis man bruker driver type ios mot Nexus, så kommer man inn, men ting feiler. Tips er å sjekke get_facts.
Output with nxos driver
Output with ios driver

## Slide 14: Q&A
Questions

## Slide 15: Extras
Ting vi ikke rekker å gå gjennom idag.

## Slide 16: Source Code fra dagens demo
https://github.com/ateanorge/CNSDQ121/tree/main/02-Harbir

## Slide 17: Install
https://napalm.readthedocs.io/en/latest/installation/
python3 -m pip install napalm
Install dependencies
  https://napalm.readthedocs.io/en/latest/installation/ios.html

## Slide 18: Integration
https://napalm.readthedocs.io/en/latest/integrations/index.html
Krever:
  napalm-ansible

## Slide 19: Other Methods
Vi rekker ikke i dagens sesjon, mer mer informasjon finnes her: https://napalm.readthedocs.io/en/latest/support/index.html#other-methods

## Slide 20: CLI Tool og Debug
Vi rekker ikke å gå gjennom i dagens sesjon, men mer informasjon finnes her:
  https://napalm.readthedocs.io/en/latest/cli.html